## Slide 1: Module 2 Introducing the workflow: Going from bacterial isolate to Genome- Synopsis of all the steps.
22 March, 2021
Anderson Oaikhena
Global Health Research Unit for Genomic Surveillance of Antimicrobial Resistance, University of Ibadan, Ibadan, Nigeria.

## Slide 2: Objectives
Discuss all processes involved in Whole Genome Sequencing, from specimen collection to generation of genome sequences.
Importance of Metadata
Details and importance of each step
Quality Control metrics at each point

## Slide 3: Overview
Specimen/
Sample
collection
Metadata- Sample/
Isolate-related information
Bacterial isolation, Identification, Antimicrobial susceptibility testing
DNA Extraction, quantification and purity checks
Library QC: qPCR, Fragment analyses.
Library pooling
Sequencing QC and analysis
Genome/Gene
Sequencing
Library preparation: construction, indexing, amplification
Inferences

## Slide 4: Metadata
Collection of information relating to samples/isolate
  Location of sampling
  Patient demographics
  Date and time of sampling and isolation
  Isolate identity and characteristics
  Antimicrobial susceptibility pattern
It is not possible to make extensive inferences about samples without comprehensive metadata
Metadata documentation is important and continuous- collected at all points, from sample collection to sequence analysis.

## Slide 5: Specimen collection
Animal samples
  Stool, blood, swabs, etc
Environmental samples
  Waste water, hospital environment e.g sinks
Food, water
  Water, food samples, soil, etc.
Human clinical samples
  Blood, stool, cerebrospinal fluid, urine, etc.
Considerations for Specimen collection
Safety considerations
  Biosafety equipment
  Patient confidentiality
Metadata
  Information relating to sampling location, type, source, etc
Sample transport
  Biosafety
  containment

## Slide 6: Bacterial isolation and Identification
Cultures consisting of isolates from a single colony
  Streaking, pour plating, spreading
Identification
  Conventional
    Gram reaction
    Colony morphology
    Manual and semi-automated biochemical tests
    MALDI-TOF
    16S rRNA sequencing
Isolate storage
  Short term: Slants, refrigeration
  Long term: freezing, ultra freezing.
Transportation of isolates: within facility, across facilities and geographical locations.
Biosafety considerations

## Slide 7: Antimicrobial Susceptibility Testing (AST)
Phenotypic methods
  Disc diffusion
  Broth microdilution
  E-test
  Semi-automated methods: Vitek/Phoenix

## Slide 8: DNA Extraction
Cell lysis
Separation of cell debris from nucleic acid
DNA isolation, purification and suspension
Different methods:
Mechanical lysis
Chemical lysis
Enzymes
Centrifugation
Chemicals
Ions
RNA degradation
Isopropanol/Ethanol
Membrane microcolumns
Magnetic beads
TE buffer/water
Phase separation: Phenol-chloroform extraction
Commercial kits: Several different kits but similar principles

## Slide 9: DNA Extraction QC: Quantity and Quality
Easy to conduct but data is not precise enough for fine analysis
Useful to infer DNA presence or absense
Useful for detecting contamination by protein, phenol, RNA
Outputs reliable DNA quantification
Requires expensive reagents
Unreliable for DNA quantification
Gel Electrophoresis
Absorbance
Fluorescence

## Slide 10: Library Preparation
Library: Total genomic DNA in the form of small pieces, usually originating from a single source.
Genomic DNA
DNA fragments
Fragments with adaptors
Amplified library
Library pool
Fragmentation
Adaptor ligation
Size selection
Amplification
Fragment analysis

## Slide 11: Sequencing
Sanger sequencing- chain termination method
Shotgun sequencing
Next generation sequencing
  Sequencing by synthesis- Illumina
  Nanopore sequencing- Oxford Nanopore Technologies
  Single molecule real time sequencing- PacBio
  454 pyrosequencing- Roche
  Semiconductor sequencing- Ion torrent

## Slide 12: Sequencing
Generating reference genomes
Sequencing individual genomes

## Slide 13: Merits of Next generation sequencing

## Slide 14: Post Sequencing
Sequencing QC
  Depth/Coverage
  Size of output
  Demultiplexing
Assembly
Sequence analysis/Bioinformatics
Inferences
Bioinformatic findings
Metadata