## Slide 1: Module 3 SARS-CoV-2 whole genome sequencing
Library Preparation using CovidSeq kits
Date : 17 May 2021
Zama Khumalo
Thabo Mohale
National Institute for Communicable Diseases, South Africa

## Slide 2: CoviSeq Library Prep Kit
The Illumina COVIDSeq™ (RUO) is a high-throughput amplicon-based NGS
Is designed to sequence the whole genome of SARS-CoV-2 using a tiling PCR approach with overlapping primers
98 primers (20-30bp)
Is based on a publicly available ARTIC protocol

## Slide 3: Library Preparation Workflow
Tagment PCR Amplicons
Post Tagmentation & Clean Up
Amplification of Tagmented Amplicons
Pooling and Purification of Libraries
Quantification & Normalization of Libraries
Pooling & Dilution of Libraries
Sequencing
Step 1
Step 2
Step 3
Step 4
Day 1
Day 2
Step 5
Library Prep
Loading the Run

## Slide 4: STEP 1
Tagment PCR Amplicons
Post Tagmentation & Clean Up
Amplification of Tagmented Amplicons
Process that fragments and tags the PCR amplicons with adapter sequences
This step washes the adapter-tagged amplicons before PCR amplification (TSB – Tagmentation Stop Buffer)
PCR amplification using unique index adapters
(Set 1-4 -multiplexing)

## Slide 5: STEP 2
Pooling &
Purification of Libraries
1
2
3
4
Pool libraries from each 96-well plate into an Eppendorf tube
Libraries of optimal size are then bound to magnetic beads, and fragments that are too small or large are wash away (80% EtoH)

## Slide 6: STEP 3
Quantification & Normalization of Libraries
Quantification of library pool using a Qubit dsDNA HS Assay kit.
Fragment analysis using TapeStation 4200
350 bp
1 2 3 4
ng/ul
Final Concentration = 4nM

## Slide 7: STEP 4
Pooling of normalized Libraries
1 2 3 4
Pool normalized libraries into 1 tube
This step produces a final pool of 384 samples diluted to a starting concentration of 4 nM
Libraries are ready to be denatured and diluted to the final loading concentration (1.4 pM)

## Slide 8: STEP 5
Sequencing
Denaturation
Pooled libraries are denatured (0.2N NaOH) to create single strands ready for sequencing
Dilute denatured libraries to 20 pM using Hybridization Buffer
The 20 pM is further diluted to 1.4pM
Final Concentration | 1.4
 | pM (µL)
20 pM denatured DNA library | 91
Pre-chilled HT1 | 1207
20 pM PhiX* control spike-in (2%) | 2
Total Volume | 1300
*PhiX- well-characterized bacteriophage genome